## Slide 1
TDMA Schedule Planner and Optimizer
Distance-2 graph colouring with spatial reuse, and an EMANE bridge
Sudarshan V | Vaan Megam Networks internship task | 1 October 2026

## Slide 2
Problem and model
Direct link (1 hop)
A
B
A and B must use different slots
Hidden terminal (2 hops)
A
B
C
A and C cannot hear each other but collide at B
Two radios conflict exactly when they are 1 or 2 hops apart.
That is the graph G2, so scheduling = vertex colouring of G2.
Colour = time slot; number of colours = frame length
Nodes 3+ hops apart reuse a slot (spatial reuse)
Radios are linked if within 500 m
Minimum colouring is NP-hard, so heuristics plus a bound

## Slide 3
Algorithm pipeline
1
Graph
networkx graph, edge if distance <= 500 m
2
Conflict graph
Connect pairs within 1 or 2 hops (G squared)
3
Heuristic
DSATUR, 300 restarts, local search that empties the top slot
4
Exact check
Branch and bound asks: are k-1 slots possible?
5
Verify
Independent re-check from raw coordinates
Lower bound = largest clique of G squared. If the result equals it, the schedule is provably optimal.

## Slide 4
Results
9
slots for the 16-node grid, proven optimal
1.78x
capacity gain over token passing (16 slots)
7.77
mean optimum on 150 random networks (2.13x gain)
76
tests pass, zero conflicts in the verifier
Demo: 4 x 4 grid, 300 m spacing, range 500 m. Random: 150 networks, 16 nodes in a 1500 m square. 80 nodes solve to optimal in 0.5 s.

## Slide 5
Spatial reuse in action
Corners 01, 04, 13, 16 share slot 8 although 900 m apart.
Radio range changes the frame length (same grid):
Range (m) | Slots
250 | 1
350 | 5
500 | 9
650 | 12
850+ | 16

## Slide 6
Part 2: EMANE bridge
schedule.json
>
emane_bridge.py
>
schedule.xml + scenario.eel
>
emaneevent-tdmaschedule
Mapping
Node_NN becomes NEM id NN
1 frame, 1000 us slots, slots = frame length
One element per slot lists every transmitting NEM
Pathloss events (80 / 200 dB) match the 500 m model
Verification plan
scheduleAcceptFull and ScheduleInfoTable per NEM
Traffic between nodes 01 and 16 (same slot, far apart) is received
Tx and Rx slot status tables show no missed slots
Status: bridge tested; EMANE runtime not yet executed

## Slide 7
Limitations and next steps
1
Disk model
Real links have SINR and fading; use EMANE packet completion curves
2
Static nodes
Recolour only the affected 2-hop neighbourhood when a node moves
3
One slot per node
Link scheduling weighted by traffic demand for unicast
4
One frequency
Multi-channel reuse could shorten the frame further